## Slide 1
OSI Network Model
IP’s
MACs
Routes
ARP
Tables
Switch
Router
Reverse Proxy
DNS
NAT
Topics Covered

## Slide 2
Analyzing Network Traffic Across …
Router
Reverse Proxy
Basic Switch

## Slide 3
Client
IP -- 192.168.13.5/24
MAC – XX:XX:XX:XX:XX:XX
Server
IP -- 192.168.13.11/24
MAC – YY:YY:YY:YY:YY:YY
Basic Switch
IP – N/A
MAC – N/A
Default Route – N/A
ping <ip>
traceroute <ip>
arp –a
route –n or netstat –rn
tcpdum -i any -w /mnt/test.pcap
LAN
eth0
eth0
L2 Switch
Forwarding (MAC) Table
ARP Table
Route Table
ARP Table
Route Table
eth0
eth1
Internet
IP -- 192.168.14.1
MAC – AB:AB:AB:AB:AB:AB
Notes: 1: arp –a
2: Client : “ping 192.168.13.11”
FOR SSL CERT
echo | openssl s_client -showcerts -servername gnupg.org -connect gnupg.org:443 2>/dev/null | openssl x509 -inform pem -noout -text
In your example you have PC1 (10.0.0.1) connected to fa0/1 and PC2 (10.0.0.2) connected to fa0/2, imagine a ping request from PC1 to PC2 in this scenario.
1. PC1 - ping 10.0.0.2, PC1 does not currently have an entry in the arp table for this ip address so it sends a broadcast arp request, asking "who has ip address 10.0.0.2? what is your mac address"
2. SW1 sees this arp request, the first thing it does is make an entry in it's mac-address table for PC1's ip to mac translation and marks it reachable via fa0/1. Now SW2 forwards the arp broadcast out every other available port, except the port on which it was recieved (this action is know as flooding)
3. PC2 sees the arp broadcast and replies with an arp unicast response to PC1 containing PC2's ip address and mac-address.
4. SW2 sees this arp response so it makes an entry in it's mac-address table for PC2's ip to mac translation, and marks it reachable via fa0/2.
Example from "show arp". The IP address is matched to the Mac Address
Internet 192.168.200.3 3 0007.dddd.abc2 ARPA Vlan4 Internet 192.168.200.10 6 000a.bbbb.a5ba ARPA Vlan4 Internet 192.168.200.17 - 0014.cccc.6c7b ARPA Vlan5 Internet 192.168.200.25 208 0005.aaaa.3b5a ARPA Vlan5
The mac-address-table Maps Mac Addresses to Physical Ports on a Switch
Example from "show mac-address-table" The Mac address is matched with the port Number.
MAC Address Port the MAC was learned on
0021.d837.a6fc Dynamic 1 FastEthernet3 0007.95dc.04c1 Dynamic 4 FastEthernet2
000a.95b0.a5aa Dynamic 4 FastEthernet0
5.. PC1 eventually get the arp response from PC2 and packages the initial ping request with the correct mac-address for PC2
A L2 switch generally only has an IP address for remote management purposes and it is assigned to a virtual interface (such as vlan 1).

## Slide 4
Client
IP -- 192.168.13.5/24
MAC – XX:XX:XX:XX:XX:XX
Server
IP -- 192.168.14.11/24
MAC – YY:YY:YY:YY:YY:YY
Basic Switch
IP – N/A
MAC – N/A
ping <ip>
traceroute <ip>
arp –a
route –n or netstat –rn
tcpdum -i any -w /mnt/test.pcap
eth0
eth0
L2 Switch
Forwarding (MAC) Table
ARP Table
Route Table
ARP Table
Route Table
eth0
eth1
BACKEND
CLIENT
Notes: In your example you have PC1 (10.0.0.1) connected to fa0/1 and PC2 (10.0.0.2) connected to fa0/2, imagine a ping request from PC1 to PC2 in this scenario.
1. PC1 - ping 10.0.0.2, PC1 does not currently have an entry in the arp table for this ip address so it sends a broadcast arp request, asking "who has ip address 10.0.0.2? what is your mac address"
2. SW1 sees this arp request, the first thing it does is make an entry in it's mac-address table for PC1's ip to mac translation and marks it reachable via fa0/1. Now SW2 forwards the arp broadcast out every other available port, except the port on which it was recieved (this action is know as flooding)
3. PC2 sees the arp broadcast and replies with an arp unicast response to PC1 containing PC2's ip address and mac-address.
4. SW2 sees this arp response so it makes an entry in it's mac-address table for PC2's ip to mac translation, and marks it reachable via fa0/2.
Example from "show arp". The IP address is matched to the Mac Address
Internet 192.168.200.3 3 0007.dddd.abc2 ARPA Vlan4 Internet 192.168.200.10 6 000a.bbbb.a5ba ARPA Vlan4 Internet 192.168.200.17 - 0014.cccc.6c7b ARPA Vlan5 Internet 192.168.200.25 208 0005.aaaa.3b5a ARPA Vlan5
The mac-address-table Maps Mac Addresses to Physical Ports on a Switch
Example from "show mac-address-table" The Mac address is matched with the port Number.
MAC Address Port the MAC was learned on
0021.d837.a6fc Dynamic 1 FastEthernet3 0007.95dc.04c1 Dynamic 4 FastEthernet2
000a.95b0.a5aa Dynamic 4 FastEthernet0
5.. PC1 eventually get the arp response from PC2 and packages the initial ping request with the correct mac-address for PC2
A L2 switch generally only has an IP address for remote management purposes and it is assigned to a virtual interface (such as vlan 1).

## Slide 5
Client
IP -- 192.168.13.5
MAC – XX:XX:XX:XX:XX:XX
Default Route – 192.168.13.1
Route – 192.168.14.0/24 VIA 192.168.13.10
Server
IP -- 192.168.14.11
MAC – YY:YY:YY:YY:YY:YY
Default Route – 192.168.14.1
Route – 192.168.13.0/24 VIA 192.168.14.10
Router
IP – 192.168.13.10
MAC – AA:AA:AA:AA:AA:AA
IP – 192.168.14.10
MAC – BB:BB:BB:BB:BB:BB
Default Route – 192.168.14.1
ping <ip>
traceroute <ip>
arp –a
route –n or netstat –rn
tcpdum -i any -w /mnt/test.pcap
BACKEND
CLIENT
eth0
eth0
eth1
eth0
Internet
IP -- 192.168.13.1
MAC – AB:AB:AB:AB:AB:AB
Internet
IP -- 192.168.14.1
MAC – BA:BA:BA:BA:BA:BA
L3 Routing
ARP Table
Route Table
ARP Table
Route Table
Notes: Summary of activities :
On Client:
- arp -n
- ping 8.8.8.8
- traceroute 8.8.8.8
- netstat -rn
- curl http://ping.sl.americasreadiness.com
Modify routes on Client :
  route del -net 0.0.0.0 gw 192.168.13.1 netmask 0.0.0.0 dev eth0
  route add -net 0.0.0.0/0 gw 192.168.13.10 dev eth0
    OR route add -net 192.168.14.0/24 gw 192.168.13.10 dev eth0
      ASK : what’s the difference?
Modify routed on Server:
  route del -net 0.0.0.0 gw 192.168.14.1 netmask 0.0.0.0 dev eth0
  route add -net 0.0.0.0/0 gw 192.168.14.10 dev eth0
    OR route add -net 192.168.13.0/24 gw 192.168.14.10 dev eth0
      ASK : what’s the difference?
Packet capture on the Router for PING traffic and CURL traffic

## Slide 6
SWITCH
Home Router
eth1
eth0
ROUTER

## Slide 7
SWITCH
Home Router
eth1
WAN
ROUTER
INTERNET

## Slide 8
Client
IP -- 192.168.13.5
MAC – XX:XX:XX:XX:XX:XX
Default Route – 192.168.13.1
Servers
IPs -- 192.168.14.11-12
MACs – XY:XY:XY:XY:XY:XY
Default Route – 192.168.14.1
ping <ip>
traceroute <ip>
arp –a
route –n or netstat –rn
tcpdum -i any -w /mnt/test.pcap
BACKEND
CLIENT
eth0
eth0
eth0
Internet
IP -- 192.168.13.1
MAC – AB:AB:AB:AB:AB:AB
Internet
IP -- 192.168.14.1
MAC – BA:BA:BA:BA:BA:BA
Proxy (2 Arm)
VIP – 192.168.13.10
MAC – AA:AA:AA:AA:AA:AA
SNIP – 192.168.14.10
MAC – BB:BB:BB:BB:BB:BB
Default Route – 192.168.14.1
Reverse Proxy
eth2
eth1
Air Gap
NSIP – 192.168.15.10
eth0
Notes: No activities. Current Docker set up is broken for CPX proxy in two arm mode.
Only discussion covering :
- NS IP
VIP

## Slide 9
Advanced Networking
Basic Switch
Router Firewall
Reverse Proxy

## Slide 10
ping <ip>
traceroute <ip>
arp –a
route –n or netstat –rn
tcpdum -i any -w /mnt/test.pcap
BACKEND
CLIENT
Client
IP -- 192.168.13.5
MAC – XX:XX:XX:XX:XX:XX
Default Route – 192.168.13.10
eth0
Server
IP -- 192.168.14.11
MAC – YY:YY:YY:YY:YY:YY
Default Route – 192.168.14.10
eth0
eth1
eth2
eth1
eth0
Router-1 (Edge)
IP – 192.168.13.10
MAC – AA:AA:AA:AA:AA:AA
IP – 192.168.15.10
MAC – BB:BB:BB:BB:BB:BB
IP – 192.168.16.10
MAC – BC:BC:BC:BC:BC:BC
Default Route – 192.168.16.1
Router-2
IP – 192.168.14.10
MAC – CC:CC:CC:CC:CC:CC
IP – 192.168.15.100
MAC – DD:DD:DD:DD:DD:DD
Default Route – 192.168.15.10
Internet
IP – 192.168.16.1
MAC – AB:AB:AB:AB:AB:AB
eth0
DMZ/Firewall
DMZ
Notes: Summary of activities :
On Client:
- arp -n
- ping 8.8.8.8
- traceroute 8.8.8.8
- netstat -rn
- curl http://ping.sl.americasreadiness.com
Modify routes on Client :
  route del -net 0.0.0.0 gw 192.168.13.1 netmask 0.0.0.0 dev eth0
  route add -net 0.0.0.0/0 gw 192.168.13.10 dev eth0
    OR route add -net 192.168.14.0/24 gw 192.168.13.10 dev eth0
      ASK : what’s the difference?
Modify routes on Server-a and Server-b:
  route del -net 0.0.0.0 gw 192.168.14.1 netmask 0.0.0.0 dev eth0
  route add -net 0.0.0.0/0 gw 192.168.14.10 dev eth0
    OR route add -net 192.168.13.0/24 gw 192.168.14.10 dev eth0
      ASK : what’s the difference?
Modify routes on Routers via GUI
Packet capture on the Router for PING traffic and CURL traffic
Block ICMP traffic and show PING fails but CURL works.

## Slide 11
ping <ip>
traceroute <ip>
arp –a
route –n or netstat –rn
tcpdum -i any -w /mnt/test.pcap
BACKEND
CLIENT
Client
IP -- 192.168.13.5
MAC – XX:XX:XX:XX:XX:XX
Default Route – 192.168.13.10
eth0
Servers
IPs -- 192.168.14.11-12
MACs – XY:XY:XY:XY:XY:XY
Default Route – 192.168.14.10
eth0
eth1
eth2
eth1
eth0
Router-1
IP – 192.168.13.10
MAC – AA:AA:AA:AA:AA:AA
IP – 192.168.15.10
MAC – BB:BB:BB:BB:BB:BB
IP – 192.168.16.10
MAC – BC:BC:BC:BC:BC:BC
Default Route – 192.168.16.1
Router-2
IP – 192.168.14.10
MAC – CC:CC:CC:CC:CC:CC
IP – 192.168.15.100
MAC – DD:DD:DD:DD:DD:DD
Default Route – 192.168.15.10
eth0
Proxy (1 Arm)
NSIP – 192.168.15.11
MAC – EE:EE:EE:EE:EE:EE
VIP – 192.168.15.13
MAC – EE:EE:EE:EE:EE:E1
SNIP – 192.168.15.12
MAC – EE:EE:EE:EE:EE:E2
Default Route – 192.168.15.10
Route – 192.168.14.0/24 VIA 192.168.15.100 to
eth0
Internet
IP – 192.168.16.1
MAC – AB:AB:AB:AB:AB:AB
eth0
Reverse Proxy 1 Arm
DMZ
Notes: FIREWALL DEMO
FORWARD table under filter
Default action : DROP
ACCEPT if source IP 192.168.15.12
ACCEPT if destination IP 192.168.15.12